## Slide 1
DeepSeek V4-Flash: PCIe 5.0 vs PCIe 6.0 NVMe Expert Offload I/O Analysis — GB10 (273 GB/s GPU BW / 123 TOPS FP16)
PCIe 6.0 x4 (32 GB/s) vs PCIe 5.0 x4 (15.75 GB/s): 2.03× load speedup; 2× cold decode (18.4 vs 9.1 tok/s). Decode transitions to GPU-memory-bound at ~37% hit (PCIe 6) vs ~67% hit (PCIe 5) — both converge to 26 tok/s GPU ceiling. Prefill/TTFT: PCIe6 only helps for C < 559 tokens (IO-bound) — TTFT 54 ms vs 110 ms at L=128; at C≥559 both CPU-bound at 5,052 tok/s ceiling.
Load
① Cold Boot: Model Load
Total model: 86.68 GB (8.76 GB dense + 77.92 GB experts)
UFS 5.0 full load: 8.67 s vs NVMe 7 GB/s: 12.38 s → 1.43× faster
Dense-only hot path: 0.88 s → inference ready in <1 s
T = model_size / storage_BW
UFS 5.0: 46.6 Gbps × 2 lanes → 10 GB/s payload
Speedup = 10 / 7 = 1.43× (load independent of GPU specs)
Chart: Cold Boot Load Time (seconds)
| UFS 5.0 10 GB/s | NVMe 7 GB/s
Load Time (s) | 8.67 | 12.38
Prefill
② Prefill: Layer Pipeline IO vs Compute
IO/layer PCIe5: 6×6.75MB/15.75 GB/s = 2.57 ms
IO/layer PCIe6: 6×6.75MB/32 GB/s = 1.27 ms
Compute/layer (123T, C=2K): 9.43 ms Crossover: PCIe5≥559, PCIe6≥275 tok
C | CPU/layer | PCIe5 TPS | Regime | PCIe6 TPS | Regime
128 | 0.59ms | 1,158 | IO✗ | 2,352 | IO✗
275★ | 1.27ms | 2,488 | IO✗ | 5,052 | cross✓
512 | 2.36ms | 4,631 | IO✗ | 5,052 | CPU✓
559★ | 2.57ms | 5,052 | cross✓ | 5,052 | CPU✓
≥1,024 | ≥4.71ms | 5,052 | CPU✓ | 5,052 | CPU✓
TTFT — Prompt Length L | PCIe5 TTFT | PCIe6 TTFT | Δ
L≤256 (both IO-bnd) | 110.5 ms | 54.4 ms ★ | 2.03× faster
L=512 P5=IO; P6=CPU | 110.5 ms | 101.4 ms | 1.09× faster
L≥559 (both CPU-bnd) | ~405 ms / 2K-tok | ~405 ms / 2K-tok | 1.0× (tied)
Decode
③ Decode: Hot Cache × Storage BW
Expert IO/token: 258(6×43) × 6.75 MB = 1.74 GB
Dense (GPU mem): 8.76 GB / 273 GB/s = 32.1 ms (always overlapped)
Hot Cache | Cold (GB) | PCIe5 ms | PCIe5 TPS | PCIe6 ms | PCIe6 TPS
0% | 1.74 | 110.5 | 9.1 | 54.4 | 18.4
30% | 1.22 | 77.4 | 12.9 | 38.1 | 26.2
50% | 0.87 | 55.3 | 18.1 | 35.3 | 28.3
70% | 0.52 | 36.6 | 27.3 | 36.6 | 27.3
85% | 0.26 | 37.5 | 26.7 | 37.5 | 26.7
100% | 0.000 | 38.5 | 26.0 | 38.5 | 26.0
PCIe5→GPU-bnd: ~67% hit | PCIe6→GPU-bnd: ~37% hit | GPU ceil = 26.0 tok/s (273 GB/s fixed)
Chart: 
| 0% | 30% | 50% | 70% | 85% | 100%
PCIe 5.0 | 9.1 | 12.9 | 18.1 | 27.3 | 26.7 | 26
PCIe 6.0 | 18.4 | 26.2 | 28.3 | 27.3 | 26.7 | 26
GPU Ceil | 26 | 26 | 26 | 26 | 26 | 26
Performance Summary: PCIe 5.0 x4 (15.75 GB/s) vs PCIe 6.0 x4 (32 GB/s) NVMe — ds4 FlashMoE on GB10 (273 GB/s / 123 TOPS)
Scenario | PCIe 5.0 (15.75 GB/s) | PCIe 6.0 (32 GB/s) | Improvement | Bottleneck
Cold Boot | 20.55 s | 10.12 s | 2.03× faster | Storage BW (I/O-bound both)
Prefill C=128 | 1,158 tok/s | 2,352 tok/s | 2.03× | IO-bound (expert load/layer: PCIe5=2.57ms, PCIe6=1.27ms)
Prefill C≥559 ★ | 5,052 tok/s | 5,052 tok/s | = CPU-bnd | Compute ceiling: 123T ÷ (43×566M) = 5,052 tok/s (tied)
Decode 0% hot | 9.1 tok/s | 18.4 tok/s | 2.03× | Cold NVMe bottleneck
Decode ~50% hot | 18.1 tok/s | 28.3 tok/s ★ | PCIe6 peak | PCIe5=SSD-bnd; PCIe6=GPU-bnd (peak at ~37% hit)
Decode ≥70% hot | ~27 tok/s | ~27 tok/s | ≈1.0× (tied) | GPU memory ceiling (both) @ 273 GB/s
TTFT L≤256 | 110.5 ms | 54.4 ms ★ | 2.03× faster | IO-bound (same expert-load BW as decode cold path)
TTFT L=512 | 110.5 ms | 101.4 ms | 1.09× faster | PCIe5=IO-bnd (C<559); PCIe6=CPU-bnd (C>275)
TTFT L≥559 (C=2K) | ~405 ms/2K | ~405 ms/2K | 1.0× (tied) | CPU-bound — NVMe upgrade won't shorten prefill latency
* GB10: 273 GB/s GPU mem BW, 123 TOPS FP16. ds4 FlashMoE: 43 layers, 256 experts/layer, 6 active, expert=6.75 MB (Q4). PCIe 5.0 x4: 15.75 GB/s; PCIe 6.0 x4: 32 GB/s. Prefill TPS ceiling: 123T÷(43×566.2M)=5,052 tok/s; PCIe6 IO→CPU crossover C=275, PCIe5 C=559. TTFT(L)=43×max(IO/layer, L×4.603µs/layer): PCIe5 IO-bnd TTFT=110.5 ms fixed for L<559; PCIe6 IO-bnd TTFT=54.4 ms for L<275. Decode: PCIe5→GPU-bnd@~67% hit; PCIe6→GPU-bnd@~37%; GPU ceil=26 tok/s.