## Slide 1
GB10 ds4 Performance Update
Measured on GB10 · 273 GB/s · 123 TOPS
① Cold Boot: Model Load
Load
② Prefill: Resident BW + Context Compute
Prefill
③ Decode: UMA Weights + Long Context
Decode
Total model: 80.76 GB (8.16 GB dense + 72.6 GB experts)
PCIe 6.0 x4: 32 GiB/s vs PCIe 5.0 x4: 15.75 GiB/s → 2.03× faster
IO BW utilization: 56% (measured on GB10)
T = Model_Size / (BW × Utilization)
PCIe 6.0 x4: 80.76 / (32 × 0.56) = 4.51 s
PCIe 5.0 x4: 80.76 / (15.75 × 0.56) = 9.16 s
Speedup = 9.16 / 4.51 = 2.03×
Updated conclusion
Cold Boot is SSD/NVMe → UMA/DDR loading. With measured 56% IO efficiency, PCIe 6.0 x4 reduces startup from 9.16 s to 4.51 s.
Calculation logic
η_mem,prefill = [ceil(P/2048) × 80.76 / prefill_s] / 273
m = mem / (mem + gpu), c = gpu / (mem + gpu)
Pred(273/120)=Obs/(m+c×123/120); Pred(546/120)=Obs/(0.5m+c×123/120)
Context
GB10 TPS
Mem Util
GPU Busy
273GB/120T
546GB/120T
128
148.98
34.43%
0.00%
148.98
297.96
1,024
379.51
10.96%
5.00%
376.56
571.18
2,048
396.40
5.73%
7.00%
391.02
502.55
8,192
390.78
5.64%
9.90%
384.65
468.33
65,536
336.37
4.86%
87.08%
328.59
337.30
131,072
290.63
4.20%
92.05%
283.84
290.02
Updated conclusion
Small-context Prefill is resident-bandwidth dominated, so 546 GB/s nearly doubles 128-token throughput. At 64K–128K, context compute dominates and extra bandwidth adds little.
Calculation logic
Active weights/token = 10.97 GiB = 8.20 + 1.07 + 72.56×6/256
η_mem,decode = generation_tps × 10.97 / 273
Pred(273/120)=Obs/(m+c×123/120); Pred(546/120)=Obs/(0.5m+c×123/120)
Context
GB10 TPS
Mem Util
GPU Busy
273GB/120T
546GB/120T
128
16.12
64.78%
8.62%
16.07
28.70
1,024
15.26
61.32%
8.29%
15.21
27.13
2,048
14.58
58.59%
8.13%
14.54
25.85
8,192
14.36
57.70%
94.38%
14.14
17.39
65,536
12.25
49.22%
96.00%
12.05
14.46
131,072
10.73
43.12%
96.00%
10.55
12.44
Updated conclusion
Decode is dominated by UMA-weight and KV/state bandwidth. Doubling bandwidth helps short contexts strongly, but long-context gains compress to ~15–20% as context-path overhead grows.
Performance Summary: GB10 Measured vs Next-Gen Memory/Compute Configs
Scenario
GB10 (273/123T)
Next A (273/120T)
Next B (546/120T)
Improvement
Bottleneck
Cold Boot
9.16 s
9.16 s
9.16 s
same
Storage BW only (NVMe/PCIe path; UMA/compute unchanged)
Prefill C=128
148.98 tok/s
148.98 tok/s
297.96 tok/s
2.00× @ 546GB
Resident UMA BW + fixed cost
Prefill C=2,048 ★
396.40 tok/s
391.02 tok/s
502.55 tok/s
1.27× @ 546GB
Hybrid (resident BW + compute)
Decode @128 ctx
16.12 tok/s
16.07 tok/s
28.70 tok/s
1.78× @ 546GB
UMA active-weight bandwidth
Decode @8K ctx
14.36 tok/s
14.14 tok/s
17.39 tok/s
1.21× @ 546GB
Mixed (memory + context path)
Decode @128K ctx
10.73 tok/s
10.55 tok/s
12.44 tok/s
1.16× @ 546GB
Long-context KV/state + compute path