## Slide 1
GB10 ds4 Performance Update
Measured on GB10 · 273 GB/s · 123 TOPS
① Cold Boot: Model Load
Load
② Prefill: Resident BW + Context Compute
Prefill
③ Decode: UMA Weights + Long Context
Decode
Total model: 80.76 GB (8.16 GB dense + 72.6 GB experts)
PCIe 6.0 x4: 32 GiB/s vs PCIe 5.0 x4: 15.75 GiB/s → 2.03× faster
IO BW utilization: 56% (measured on GB10)
T = Model_Size / (BW × Utilization)
PCIe 6.0 x4: 80.76 / (32 × 0.56) = 4.51 s
PCIe 5.0 x4: 80.76 / (15.75 × 0.56) = 9.16 s
Speedup = 9.16 / 4.51 = 2.03×
Updated conclusion
Cold Boot is SSD/NVMe → UMA/DDR loading. With measured 56% IO efficiency, PCIe 6.0 x4 reduces startup from 9.16 s to 4.51 s.
Calculation logic
η_mem,prefill = [ceil(P/2048) × 80.76 / prefill_s] / 273
m = mem / (mem + gpu), c = gpu / (mem + gpu)
Pred(273/120)=Obs/(m+c×123/120); Pred(546/240)=Obs/(0.5m+c×123/240)
Context
GB10 TPS
Mem Util
GPU Busy
273GB/120T
546GB/240T
128
148.98
34.43%
0.00%
148.98
297.96
1,024
379.51
10.96%
5.00%
376.56
753.12
2,048
396.40
5.73%
7.00%
391.02
782.05
8,192
390.78
5.64%
9.90%
384.65
769.31
65,536
336.37
4.86%
87.08%
328.59
657.18
131,072
290.63
4.20%
92.05%
283.84
567.69
Updated conclusion
Small-context Prefill is resident-bandwidth dominated, so 546 GB/s nearly doubles 128-token throughput. With 240T compute, long-context Prefill also scales strongly because bandwidth and context compute both improve.
Calculation logic
Active weights/token = 10.97 GiB = 8.20 + 1.07 + 72.56×6/256
η_mem,decode = generation_tps × 10.97 / 273
Pred(273/120)=Obs/(m+c×123/120); Pred(546/240)=Obs/(0.5m+c×123/240)
Context
GB10 TPS
Mem Util
GPU Busy
273GB/120T
546GB/240T
128
16.12
64.78%
8.62%
16.07
32.15
1,024
15.26
61.32%
8.29%
15.21
30.43
2,048
14.58
58.59%
8.13%
14.54
29.07
8,192
14.36
57.70%
94.38%
14.14
28.28
65,536
12.25
49.22%
96.00%
12.05
24.10
131,072
10.73
43.12%
96.00%
10.55
21.10
Updated conclusion
Decode is dominated by UMA-weight and KV/state bandwidth. With 546 GB/s plus 240T, short-context Decode approaches 2x, while long-context Decode still benefits materially despite context-path overhead.
Performance Summary: GB10 Measured vs Next-Gen Memory/Compute Configs
Scenario
GB10 (273/123T)
Next A (273/120T)
Next B (546/240T)
Improvement
Bottleneck
Cold Boot
9.16 s
9.16 s
9.16 s
same
Storage BW only (NVMe/PCIe path; UMA/compute unchanged)
Prefill C=128
148.98 tok/s
148.98 tok/s
297.96 tok/s
2.00× @ 546/240T
Resident UMA BW + fixed cost
Prefill C=2,048 ★
396.40 tok/s
391.02 tok/s
782.05 tok/s
1.97× @ 546/240T
Hybrid (resident BW + compute)
Decode @128 ctx
16.12 tok/s
16.07 tok/s
32.15 tok/s
1.99× @ 546/240T
UMA active-weight bandwidth
Decode @8K ctx
14.36 tok/s
14.14 tok/s
28.28 tok/s
1.97× @ 546/240T
Mixed (memory + context path)
Decode @128K ctx
10.73 tok/s
10.55 tok/s
21.10 tok/s
1.97× @ 546/240T
Long-context KV/state + compute path